- Contractor shall implement inlet protection devices and Reinforced Filter Fabric barrier along road and side ditches at locations shown on the typical Storm Water Pollution Prevention (SWPP) plans to keep silt and or excavated materials from entering into the storm water inlets and ditches eventually polluting the receiving storm.

- During the excavation phase of the project, Contractor shall schedule the work in short segments so that excavation material can be quickly hauled away from the site and to prevent it from staying uncollected on the existing pavement. Any loose excavated material which falls on pavements or driveways shall be swept back into the excavated area.

- Contractor shall clean up the existing street intersections and driveways daily, as necessary, to remove any excess mud, silt or rock tracked form the excavated area.

- Contractor shall follow good housekeeping practices during the construction of the project, always cleaning up dirt and loose material as construction progresses.

- Contractor to inspect and maintain the areas listed below at least once every fourteen (14) calendar days and within 24 hours of the end of a storm event of 0.5 inches or greater.

- Disturbed areas of the construction site that have not been finally stabilized.

- Areas used for storage of materials that are exposed to precipitation.

- Structural control measures.

- Locations where vehicles enter or exit the site.

- Contractor to be responsible to maintain existing ditches and or culverts for unobstructed drainage at all times. Where sodding is disturbed by excavation on backfilling operations, such areas shall be replaced by seeding or sodding. Slopes 4:1 or steeper shall be replaced by block sodding.